## Slide 1
Manipulator dynamics
01
A simple approach for ECE students
Single-link torque, energy methods, and coding activities
Craig Chapter 6 · Bridge to Chapter 7
Notes: Two meetings of about 50 minutes. Meeting 1 slides 1–9: physical torque, inertia, holding torque, payload and Coding Activity 1. Meeting 2 slides 10–20: energy derivation, forward dynamics, motion-time preview and Coding Activity 2. Four polls total, including an opening conceptual poll whose answer is explained on slide 5. Use two coding activities, about 8 and 12 minutes. Full 2R dynamics and release simulations are outside this compact deck.

## Slide 2
A vertical-plane 1R arm
02
θ = 0°: arm hangs downward
θ = 90°: arm points right
Positive θ and τ: counterclockwise
m = 2 kg L = 0.6 m
r꜀ = L/2 = 0.3 m
g = 10 m/s²
Angles in calculations and code use radians
θ = 0°
Hangs downward
COM
θ = 90°
Positive θ
Points right
COM
Downward reference
Notes: The pivot is the joint. Yellow dot marks the center of mass. θ is measured counterclockwise from the downward vertical. Left: θ=0°, the arm hangs downward. Right: θ=90°, the arm points right. Gray dashes show the downward reference. The gold arc indicates positive rotation. Figures are schematic, with matching pose convention throughout.

## Slide 3
Q1: A stationary arm
03
The arm is stationary and horizontal. Does the motor need to produce torque?
A. Yes, to oppose gravity
B. No, because acceleration is zero
C. Only if the arm is moving
D. Only if friction is present
Poll Everywhere · Q1
Notes: Poll Q1. Allow 1–2 minutes for individual calculation. Ask pairs to compare reasoning, then reveal the next slide. Correct answer: A. At rest the inertia and viscous-friction terms vanish, but gravity remains.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 4
Inertia about the joint
04
A uniform rod has its center of mass at L/2.
The inertia about the center of mass is ICOM = mL²/12. About the joint, Ijoint = mL²/3.
Greater inertia means greater torque for the same acceleration.
Notes: If useful show parallel-axis theorem: Ijoint=Icom+m*(L/2)^2. All motion is rigid-body planar rotation.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 5
The 1R torque equation
05
Iθ̈: acceleration torque bθ̇: viscous-friction torque
mgrc sin θ: gravity torque
Use I = 0.24 kg·m² and b = 0.1 N·m·s/rad.
Q1 answer: A. At a horizontal hold, τ = mgrc = 6 N·m.
Motor torque τ
mg
r꜀
Horizontal hold
Notes: Dots are time derivatives: θdot is rad/s and θdouble-dot is rad/s². Actual gravitational torque is -mgrc*sin θ. Moving it to the required motor-torque side gives the plus sign. Actual viscous-friction torque is -b*θdot.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.
Figure: gravity acts downward at the COM. Its torque is clockwise. Positive motor torque counteracts gravity. The distance from the pivot to COM is rc. At a horizontal hold, torque is mgrc. Gold arc represents positive counterclockwise rotation.

## Slide 6
Q2: Holding at 30°
06
m = 2 kg, r꜀ = 0.3 m, g = 10 m/s².
At θ = 30°, θ̇ = 0, θ̈ = 0, what holding torque is required?
A. 0 N·m
B. 3 N·m
C. 6 N·m
D. 12 N·m
Poll Everywhere · Q2
Notes: Poll Q2. Allow 1–2 minutes for individual calculation. Ask pairs to compare reasoning, then reveal the next slide. Correct answer: B. m*g*rc*sin(30 deg)=3 N m.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 7
Q2 answer: B
07
At rest, inertia and viscous-friction terms are zero.
Gravity torque depends on the arm’s orientation.
Notes: Explain why each distractor is tempting. m*g*rc*sin(30 deg)=3 N m.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 8
A point payload at the tip
08
The gravity coefficient becomes mgrc + mp gL.
For mp = 0.5 kg: Inew = 0.24 + 0.18 = 0.42 kg·m².
Required torque: τ = Inew θ̈ + bθ̇ + (mgrc + mp gL) sin θ.
Link only
τhold = 6 N·m
0.5 kg at the tip
τhold = 9 N·m
Notes: Treat payload as a point mass rigidly attached to the tip. Additional payload rotational inertia about its own COM is neglected.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.
Figure: both arms are horizontal. The yellow COM dot belongs to the 2 kg link. The yellow square at the tip in the lower figure is an added 0.5 kg point payload. Compare 6 N m and 9 N m holding torque. Figures are schematic.

## Slide 9
Coding activity 1: Holding torque
09
Chart: Holding torque (N·m)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180
No payload | 0 | 1.0419 | 2.0521 | 3 | 3.8567 | 4.5963 | 5.1962 | 5.6382 | 5.9088 | 6 | 5.9088 | 5.6382 | 5.1962 | 4.5963 | 3.8567 | 3 | 2.0521 | 1.0419 | 0
0.5 kg payload | 0 | 1.5628 | 3.0782 | 4.5 | 5.7851 | 6.8944 | 7.7942 | 8.4572 | 8.8633 | 9 | 8.8633 | 8.4572 | 7.7942 | 6.8944 | 5.7851 | 4.5 | 3.0782 | 1.5628 | 0
Run Activity 1 in the notebook.
Report torque at 0°, 30°, 90°, 180°.
Compare payload cases and explain the curve.
8 minutes · Submit your plot and a two-sentence explanation
Notes: Expected no-payload values 0,3,6,0 N m. With 0.5 kg payload 0,4.5,9,0. At 180° ideal gravity torque is zero but equilibrium is unstable. A horizontal tabletop arm with a vertical rotation axis has no gravity torque about that axis. Complete code is provided in Activity 1, students modify parameters.

## Slide 10
Kinetic and potential energy
10
Kinetic energy measures motion.
Potential energy measures height relative to the lowest position.
The Lagrangian is ℒ = T − V.
Δh = rc
θ = 90°
θ = 0°
The COM rises by rc at 90°.
Notes: Explain that a zero reference for V is arbitrary. COM height relative to θ=0 is rc*(1-cos θ). Distinguish kinetic-energy symbol T from motion duration Tf used later.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.
Figure: the gray arm shows the downward reference pose, and the navy arm shows 90°. Yellow dots mark both COM positions. At 90° the COM rises by rc, giving V=mgrc relative to the downward pose. General rise is rc*(1-cos θ).

## Slide 11
Partial derivatives in the energy method
11
Notes: Treat angle and angular velocity as independent arguments for the partial derivatives. Hold angle fixed when differentiating with respect to velocity, and vice versa. I is constant. This is the only hand derivation required. Source: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/

## Slide 12
Forward dynamics
12
Inverse dynamics: known motion, calculate required torque.
Forward dynamics: known torque and state, calculate acceleration.
A simulation integrates acceleration to update velocity and angle.
Notes: Ask students to compare this with F=ma. Knowing torque does not determine angle immediately. The simulator uses RK4 and a small time step.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 13
Q3: The released arm
13
I = 0.24 kg·m², mgr꜀ = 6 N·m.
Release at θ = 30° with θ̇ = 0 and τ = 0. What is the initial acceleration?
A. -12.5 rad/s²
B. 0 rad/s²
C. +12.5 rad/s²
D. -25 rad/s²
Poll Everywhere · Q3
Notes: Poll Q3. Allow 1–2 minutes for individual calculation. Ask pairs to compare reasoning, then reveal the next slide. Correct answer: A. Acceleration=(0-6*sin(30 deg))/0.24=-12.5 rad/s^2.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 14
Q3 answer: A
14
The negative acceleration initially moves the arm toward θ = 0.
At release, viscous-friction torque is zero because velocity is zero.
Notes: Explain why each distractor is tempting. Acceleration=(0-6*sin(30 deg))/0.24=-12.5 rad/s^2.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 15
A preview of trajectory generation
15
Move from θ₀ = 0 to θf = π/2, with zero endpoint velocity.
Notes: Δθ=θf−θ0. This is a preview, not a full derivation of cubic coefficients. Valid for 0≤t≤Tf. Endpoint acceleration is nonzero and jumps when joined to a stationary hold. A quintic can impose zero endpoint acceleration.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 16
Q4: The same motion in half the time
16
A cubic rest-to-rest motion takes 1 s instead of 2 s.
How do peak absolute velocity and acceleration change?
A. Velocity ×2, acceleration ×2
B. Velocity ×2, acceleration ×4
C. Velocity ×4, acceleration ×2
D. Both unchanged
Poll Everywhere · Q4
Notes: Poll Q4. Allow 1–2 minutes for individual calculation. Ask pairs to compare reasoning, then reveal the next slide. Correct answer: B. For unchanged normalized path, velocity scales as 1/T and acceleration as 1/T^2.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 17
Q4 answer: B
17
Velocity scales as 1/Tf, and acceleration as 1/Tf².
Inertial torque quadruples. Total torque need not quadruple.
Notes: Explain why each distractor is tempting. For unchanged normalized path, velocity scales as 1/T and acceleration as 1/T^2.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 18
Coding activity 2: Motion time and torque
18
Run Activity 2. Compare 0° to 90° motions in 2 s and 1 s.
Report peak |θ̇|, |θ̈|, inertial torque and total torque.
Check a ±6 N·m joint torque limit, including the final hold.
Repeat with a 0.5 kg tip payload. Explain whether slowing helps.
12 minutes · Submit plots, peak values, and a feasibility conclusion
Notes: 12 minutes. Required torque is calculated for the desired path, not a simulated tracking controller. Check code peaks including endpoint values. Cubic acceleration is nonzero at endpoints. The final hold is a separate state. Sampled feasibility under an ideal symmetric limit is not hardware validation.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.

## Slide 19
Motion-time comparison
19
Chart: Required torque (N·m)
| 0 | 0.025 | 0.05 | 0.075 | 0.1 | 0.125 | 0.15 | 0.175 | 0.2 | 0.225 | 0.25 | 0.275 | 0.3 | 0.325 | 0.35 | 0.375 | 0.4 | 0.425 | 0.45 | 0.475 | 0.5 | 0.525 | 0.55 | 0.575 | 0.6 | 0.625 | 0.65 | 0.675 | 0.7 | 0.725 | 0.75 | 0.775 | 0.8 | 0.825 | 0.85 | 0.875 | 0.9 | 0.925 | 0.95 | 0.975 | 1
2 s motion | 0.56549 | 0.56608 | 0.59965 | 0.66443 | 0.75861 | 0.88032 | 1.0276 | 1.1984 | 1.3905 | 1.6015 | 1.829 | 2.0701 | 2.3221 | 2.5819 | 2.8464 | 3.1126 | 3.3772 | 3.6372 | 3.8896 | 4.1315 | 4.3605 | 4.5741 | 4.7705 | 4.9482 | 5.106 | 5.2431 | 5.3595 | 5.4551 | 5.5307 | 5.5872 | 5.6258 | 5.6482 | 5.6562 | 5.6518 | 5.6369 | 5.6138 | 5.5842 | 5.5501 | 5.5131 | 5.4742 | 5.4345
1 s motion | 2.2619 | 2.1892 | 2.1488 | 2.1391 | 2.1582 | 2.2042 | 2.2752 | 2.3691 | 2.4838 | 2.6168 | 2.7656 | 2.9275 | 3.0996 | 3.279 | 3.4626 | 3.6472 | 3.8296 | 4.0069 | 4.1759 | 4.3339 | 4.4783 | 4.6068 | 4.7175 | 4.8089 | 4.8798 | 4.9295 | 4.9577 | 4.9648 | 4.9511 | 4.9177 | 4.8659 | 4.7973 | 4.7137 | 4.6171 | 4.5095 | 4.393 | 4.2695 | 4.1408 | 4.0086 | 3.8741 | 3.7381
At the same s:
Gravity term is unchanged.
Friction term doubles.
Inertial term quadruples.
A payload needs 9 N·m at the final hold.
No payload · Both motions reach the same final pose
Notes: These curves compare corresponding points on the same normalized path, not the same physical time. At s=1 the plotted torque includes deceleration. Immediately after the motion, stationary holding torque is 6 N m with no payload, or 9 N m with payload. Slowdown cannot eliminate the required static holding torque.

## Slide 20
Next: Chapter 7 trajectory generation
20
Kinematics selects the joint configuration.
Trajectory generation specifies how that configuration changes over time.
Dynamics checks the torque required for that motion.
Feedback control helps the real robot follow the desired trajectory.
Notes: Next teach cubic coefficient derivation, joint-space interpolation and velocity/acceleration profiles. Revisit endpoint acceleration and quintic trajectories. Explain that joint-space interpolation does not generally create a straight Cartesian path.
Source for energy formulation and dynamics structure: https://modernrobotics.northwestern.edu/nu-gm-book-resource/chapter-8-1-lagrangian-formulation-of-dynamics-part-1-of-2/ . All numerical examples and activities are original teaching examples.